## Slide 1: Homebrew Yeast Harvesting and Reuse
Matt Neissa
Yeast Propagation Engineer
GigaYeast Inc.

## Slide 2: About Me
From Boston, MA
BS in Microbiology from Stanford
BS in Brewing Sciences from Germany
Avid homebrewer for over a decade!
Focus on juicy (New England style) IPAs and German Lagers

## Slide 3: Benefits of Harvesting and Reusing Yeast
Better fermentations!
  Pitch more yeast with higher viability
  Shorter lag phase and faster finish
  Lower potential for contamination
  Cleaner profile through suppressed ester formation
Cost Savings
  Lowers overall cost per batch
Avoids common problem of LHBS not having the yeast you want!

## Slide 4: When should or shouldn’t you Harvest
YES
Observe a strong fermentation
Immediately after or during primary
NO
Slow or sluggish fermentation
Aged beers
Fermented under pressure (>10psi)
Dry hopped during primary*
Any off flavors or potential signs of contamination

## Slide 5: How to Harvest Yeast
Mission Critical: Everything must be clean and sanitary!
Equipment: Yeast Brink e.g. quart glass jars or other sanitary vessel with lid
Carboy / Bucket:
Rack beer to next vessel leaving the yeast cake and a little (~1L) beer on top
Swirl remaining beer to resuspend yeast cake
Pour slurry into sanitary vessel and cap loosely
Label with strain and date harvested
Conical:
Open bottom dump valve and drain yeast slurry to sanitary vessel till clear
Cap loosely
Label with strain and date harvested

## Slide 6: Storage Conditions and Time
Store jars loosely capped at fridge temps (4C / 38F)
  Do Not Freeze!
The yeast will flocculate out over time resulting in a firm yeast cake of 100-500mL of the 1L collected
Yeast is viable for 1 month post harvest but better to use before that
  Ideal is 1-2wks post harvest

## Slide 7: Re-Pitching Protocol
How old is my yeast?
  1-2wks: No need for a starter, can pitch directly and oxygenate
  2-4wks: Recommend making a vitality starter (small, 500mL (10P 1.040) stirred for 4-8hrs)
  4+wks: Need full starter 1-3L for 24-48hrs or purchase new yeast
Remove yeast from fridge and allow to warm to fermentation temperature
If needed decant off beer and swirl to resuspend yeast
  Can save some if you would like to prep a new starter for next time
Sanitize jar lid and dump into starter or fermenter
Can repeat the harvest and pitch process as many times as you would like however recommend less than 6 generations
When in doubt, better to buy new yeast and start over!

## Slide 8: Thank You and Any Questions?